## Slide 1
NEAR FIELD COMMUNICATION
M. Roland and J. Langer, "Digital Signature Records for the NFC Data Exchange Format," 2010 Second International Workshop on Near Field Communication, Monaco, 2010, pp. 71-76. doi: 10.1109/NFC.2010.10
B. Jepson, D. Coleman, and T. Igoe, 4. Introducing NDEF [Book]. Safari, 2017. [Online]. Available: https://www.safaribooksonline.com/library/view/beginning-nfc/9781449324094/ch04.html. Accessed: Feb. 2, 2017.
NFC, Forum. "NFC Forum Technical Specifications Improve RF Communication and NFC Tag Interoperability with NFC Devices." Business Wire (English) Dec. 0010: Regional Business News. Web. 1 Feb. 2017.
electrical 4 u, "Air core transformer," 2011. [Online]. Available: http://www.electrical4u.com/air-core-transformer/. Accessed: Feb. 1, 2017.
N. Forum, A. rights reserved, A. M. services, Virtual, P. P. Terms, and C. Feedback, "What are the operating modes of NFC devices? - NFC forum," NFC Forum, 2017. [Online]. Available: http://nfc-forum.org/resources/what-are-the-operating-modes-of-nfc-devices/. Accessed: Feb. 2, 2017.
REFERENCES
Near Field Communication (NFC) was developed to enable contactless transmission of data. This poster focuses on the electromechanical properties of technology that can generate a message using an Android device (smartphone) and illustrating the standardized format of a typical message facilitating the exchange (NDEF).
Fig. 1 illustrates how a controlled electric current applied to an antenna coil attached to the powered device actively generates a directed electromagnetic field. NFC technology makes use of an phenomenon called electromagnetic induction. The presence/absence of this field over time is used to logically generate a stream of binary data.
ISO/IEC 14443 specifies the characteristics of the fields to be provided for power and bi-directional communication between proximity coupling devices (PCDs) and proximity cards or objects (PICCs).
Smartphone devices that are NFC-enable operate in reader/writer mode, one of three modes defined by the NFC Forum, when interfacing with passive NFC tags. RF interfaces must be compliant with the ISO 14443 standard in order to generate, transmit, and receive messages on ISO/IEC 18000-3 air interface which describes the parameters for air interface communications at 13.56 MHz.
INTRODUCTION
AA AA AA AA AA AA AA AA AA AA 00 00 AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA 00 00 AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA
Christopher Small
N00931863@ospreys.unf.edu
CONTACT
CNT 4514C: Wireless Networks and Mobile Computing
Professor Zornitza Genova Prodanoff
Spring Term 2017
COURSE INFORMATION
AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA